## Slide 1: Eagle Rocketry Feed System Design Review
Fall 2025: Preliminary Design Review
Eagle Rocketry Team
UPDATE 2: 11/13/2025

## Slide 2: Introduction

## Slide 3: Feed System Role
Main Objective: Develop Cal State LA's first bi-propellant liquid rocket engine.
Our Goal: Design, assemble, and successfully test a pressurized Liquid Oxygen–Kerosene feed system for our eagle's rocket engine.
Responsibilities:
Design and Develop A Bi-propellant Feed System
Research & Source Components
Manufacture & Assemble Components
Design Propellant Pneumatic Pressurization Valves

## Slide 4: P&IDs – Rocket Feed Systems

## Slide 5: Eagle Rocketry Design Parameters
Rocket engine parameters & fluid flow properties are to be considered when designing a bi-propellent liquid rocket engine
Engine Parameters |  | 
FThrust | 1000 | N
PChamber | 2.28E+6 | Pa
tBurn | 10 | s
Propellant Properties |  | 
O/FO2(L)/RP-1 | 2 | 
TO2(L)/RP-1 | 3252.57 | K
MWO2(L)/RP-1 | 20.674 | kg/k-mol
γO2(L)/RP-1 | 1.1636 | J/kg-K
RO2(L)/RP-1 | 402.17 | J/kmol-K

## Slide 6: RPA – Rocket Propulsion Analysis
RPA software was utilized to optimize propellant mixture ratios, chamber/nozzle design, and rocket engine performance. The values below are for the rocket design of choice
Parameter |  | Engine | Chamber | Units
Thrust | Sea Level | 996.7 | 996.7 | N
Specific Impulse | Sea Level | 2414.77 | 2414.77 | Ns/kg
Mass Flow Rate | Total | 0.4128 | 0.4128 | kg/s
Type | Engine | Chamber | Units
Oxidizer | 0.2752 | 0.2752 | kg/s
Fuel | 0.1376 | 0.1376 | kg/s

## Slide 7: Propellant Fluid Properties
The following fluid properties for the fuel and oxidizer propellants are listed for analytical pressure drop calculations along the rocket feed system P&ID
RP-1 ‘Kerosene’ |  | 
TRP-1 | 298.1 | K
PRP-1 | 101325 | Pa
ρRP-1 | 790 | Kg/m^3
μRP-1 | 0.001078 | Pa-s
Mass Weight | 1.46 | kg
Liquid Oxygen ‘O2(L)’ |  | 
TO2(L) | 90.2 | K
PO2(L) | 101325 | Pa
ΡO2(L) | 1141.09 | Kg/m^3
μO2(L) | 0.000195 | Pa-s
Mass Weight | 2.92 | kg

## Slide 8: Friction Major Pressure Loss Variables
The minor pressure loss calculations account for the piping from the propellant tank exit up to the injector entrance for 30 in. of pipe length
Fluid Properties: RP-1 |  | 
Pipe: | ¼ in. Copper (Type K) | 
QFuel | 1.74E-4 | m^3/s
VelFuel | 5.5 | m/s
ReFuel | 25590.86 | 
e/DFuel | 0.00024 | m
fFuel | 0.0249 | 
△PFriction | 3.58E+4 | Pa
Fluid Properties: O2(L) |  | 
Pipe: | ¼ in. Copper (Type K) | 
QOxidizer | 2.41E-4 | m^3/s
VelOxidizer | 7.61 | m/s
ReOxidizer | 283515.98 | 
e/Doxidizer | 0.00024 | m
fOxidizer | 0.0167 | 
△PFriction | 6.63E+4 | Pa

## Slide 9: Friction Minor Pressure Loss Variables
The minor pressure loss calculations below account for the pipe fittings and components from the propellant tank exit up to the injector entrance.
Pipe Fittings: RP-1 |  | 
KL1 | 0.5 | Contraction
KL2 | 0.5 | Ball Valve
KL3 | 0.35 | Pneumatic
KL4 | 1.08 | Check Valve
KL5 | 1.5 | Elbow
KL6 | 2 | Tee
KL7 | 1 | Entrance
△PK_L-Total | 1.30E+5 | Pa
Pipe Fittings: O2(L) |  | 
KL1 | 0.5 | Contraction
KL2 | 0.5 | Ball Valve
KL3 | 0.35 | Pneumatic
KL4 | 1.08 | Check Valve
KL5 | 1.5 | Elbow
KL6 | 2 | Tee
KL7 | 1 | Entrance
△PK_L-Total | 3.62E+5 | Pa

## Slide 10: Orifice Restriction & Pressure Head Loss
Fluid properties entering the rocket engine are affected by the orifice entrance at the combustion chamber
Fluid properties and pressure is affected due to the height difference in the P&ID
RP-1 ‘Kerosene’ |  | 
Cd | 0.75 | 
△PK_L-Total | 2.12E+4 | Pa
Liquid Oxygen ‘O2(L)’ |  | 
Cd | 0.75 | 
△PK_L-Total | 5.88E+4 | Pa
RP-1 ‘Kerosene’ |  | 
Total Height | 0.127 | m
△PHydrostatic | 984.24 | Pa
Liquid Oxygen ‘O2(L)’ |  | 
Total Height | 0.127 | m
△PHydrostatic | 1421.65 | Pa

## Slide 11: Overview

## Slide 12: High-Level Overview
Nitrogen Pressurant Sub-system
Stores and supplies high-pressure nitrogen gas used to maintain tank and feed-line pressures in liquid propellent rocket engines.
2400 psi
S
~??? psi
S
PT
PT
To Distribution

## Slide 13: High-Level Overview
Nitrogen Distribution & Work Gas Sub-system
A network that distributes, regulates, and controls the nitrogen gas utilized for all pneumatic and pressurization tasks.
From Pressurant
PT
To Fuel
To Oxidizer
PT
150psi

## Slide 14: High-Level Overview
Fuel & Oxidizer Tank Sub-system
Isolates and controls the pressurized gas and delivers the propellants into the combustion chamber
From Distribution
P
S
S
PT
Fuel/Ox
Only present on fuel side
P
From Distribution
To Chamber
TC
3x For Oxidizer
S

## Slide 15: Full Propellant Feed System
2400 psi
S
~850 PSI
S
PT
PT
PT
PT
150 PSI
P
S
S
PT
Fuel
500 PSI
P
S
P
S
S
PT
P
S
Chamber
PT
PT
PT
TC
TC
TC
TC
TC
TC
TC
TC
Piping & Instrumentation Diagram
Nitrogen Pressuring System
Gas Distribution System
Fuel/Oxidizer Systems
Oxidizer
550 PSI

## Slide 16: Components

## Slide 17: Propellant Tanks - Design Requirements
Propellant Tanks |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 18: Propellant Tanks – Final Design Choices
Propellant Tanks |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 19: Manual Ball Valves - Design Requirements
Manual Ball Valves |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 20: Manual Ball Valves – Final Design Choices
Manual Ball Valves |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 21: Relief Valves - Design Requirements
Relief Valves |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 22: Relief Valves – Final Design Choices
Relief Valves |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 23: Check Valves - Design Requirements
Check Valves |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 24: Check Valves - Design Choices
Check Valves |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 25: Pressure Gages - Design Requirements
Pressure Gauges |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 26: Pressure Gages - Design Choices
Pressure Gauges |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 27: Pressure Transducers - Design Requirements
Pressure Transducers |  | 
Type | Design Requirement | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 28: Pressure Transducers - Design Choices
Pressure Transducers |  | 
Type | Design Choice | Units
Diameter NPT | ¼ | In.
Pressure | 2000 | PSI
Temperature | -4 to 302 | F

## Slide 29: Conclusion